## Slide 1: Expending MAM Principles to the Characterization of Cell-based Therapies
Camille Lombard-Banek, Kerstin Pohl, Edward J. Kwee, Sumona Sarkar, John T. Elliott, and John E. Schiel

## Slide 2: The role of NIST in advancing biomanufacturing
Measure to Understand and Diagnose
Gene Therapy & Viral Vectors
RNA Vaccines
mAbs
Measure to
Accelerate & Improve
Treatment Options
NIST
Measurement Tools &
Reference Materials are central to Innovation & Quality
Cancer
Genetic
Disorders
SARS COV-2
Cell Therapies
Notes: Known biological threats and ailments have not gone away and new threats such as Zika, Covid, etc. are emerging. Thankfully the arsenal of modalities to treat these illnesses is evolving with an equally unprecedented pace. We have gone from small molecules to antibodies to harnessing the actual threat (e.g. virus) as a tool in it’s own demise! To imagine that we would be potentially using an adenoviral vector to vaccinate against another virus (SARS COV-2) is astonishing.
The old adage in woodwork and building is to measure twice and cut once. Metrologists know full well, however, that nothing less than triplicate will do. In addition, we can only observe and improve what we can measure, and that measurement must be both accurate and precise.
To this end, the NIST biomanufacturing program is dedicated to accelerating measurement technologies to better understand the critical attributes of a successful therapeutic product. We develop innovative measurement tools, adapt and improve existing tools, and develop reference materials to fuel those efforts.
NIST continues to evolve with the landscape of changing treatment modalities.

## Slide 3: What are CAR T-cells?
Larson, R.C., Maus, M.V., Nat Rev Cancer, 21, 2021
Engineered T-cells to target circulating cancer cells
  Autologous: T-cell from the patient
  Allogenic: T-cell from a donor
3 FDA approved therapies (all autologous)

## Slide 4: Opportunities and challenges for proteomics on CAR T-cells
T-cell isolation
& Expansion
Transduction
CAR T-cell
Virus
Expansion
Infusion
T-cell Purity
T-cell MQAs
Gene vector MQAs
Effect on the T-cell biology
Success rate of transfection
% of CAR expressing cells
Effect on CAR-T cell biology
Success rate
% of CAR expressing cells
PK & PD evaluation
Toxicity monitoring
MoA
T-cell
Lombard-Banek, C. & Schiel J.E., Molecules, 2020
Notes: Add a slide about what CAR T is  Slide with CAR T killing cancer cell

## Slide 5: Expanding MAM principles to CAR T-cell therapies
Secreted
1 protein  200 peptides
Historical product knowledge
Not limited in quantities
NISTmAb as system suitability
Live cell  Complex material extraction
“Active ingredient” = membrane protein
10,000+ proteins  106 peptides
Limited starting material
No system suitability available

## Slide 6: Requirements for large-scale proteomics implementation for the analysis of CAR T-cell therapies
Lombard-Banek, C. & Schiel J.E., Molecules, 2020
Amenable to small protein input
 Scalable
Detect peptides from the CAR protein
   Efficient extraction of membrane proteins
Detect protein changes
  Sensitive
  Broad proteome coverage
High quantitative reproducibility
Proper instrument controls in place

## Slide 7: Workflow for large-scale proteomics implementation for CAR T-cell therapies
Lombard-Banek, C. & Schiel J.E., Molecules, 2020
NanoLC™ 425 HPLC System
TripleTOF® 6600+ LC-MS/MS System
OptiFlow® Turbo V
Ion Source
Revisions done on a commercial K562 digest

## Slide 8: Designing a sensitive and controlled acquisition method for CAR-T proteomics
Chromatography
Column:
Particle size
Length
Gradient duration
Mass Spectrometry
m/z
m/z
TOF-MS
MS/MS
s
DDA
SWATH®
m/z
m/z
Acc. time & # Precursors
Col. energ. spread
m/z
SWATH window scheme
IQ Metrics
PC
K562
Peptide Mix (e.g. PepCal)
FWHM
Ret. Times
Mass accuracy
Complex Digest (e.g. K562)
Protein ID
Quant. performances

## Slide 9: Evaluating different columns to test selectivity and performances
Metrics to evaluate:
Number of peptide identified
Types of peptides identified
Number of proteins quantified
Quality of quantification (e.g. %CV)
 Use commercial K562 digest
Column | Vendor | Particle size (µm) | Pore size (A) | Length (cm)
1 | A | 3 | 120 | 15
2 | B | 3 | 300 | 15
3 | C | 1.7 | 130 | 15
4 | C | 1.7 | 130 | 25
5 | C | 1.7 | 300 | 25
Notes: Again some bullets. Why different columns? I like the idea of presenting that we know going in that chromatographic performance and stationary phase selectivity will undoubtedly results in different peptide IDs. We were curious as to how this might differ and whether the totality of evidence from multiple runs could or should be harnessed. Then later when tou show that different columns did have different peptide IDs, the CAM-T data merger tool (Collated Acquisition Management Tool) was written.

## Slide 10: Comparison of the proteins identified with the different columns

## Slide 11: Protein quantification from SWATH® Acquisition
Low number of missing values
High dynamic range
Provides a library for future targeted assays
Ludwig, C, Aebersold R. et al., Mol Syst Biol. 2018 Aug; 14(8): e8126.
Notes: Good for quant
“all ion” allows comprehensive proteome coverage
Dynaic range?
Other?

## Slide 12: Protein identification and quantification from SWATH® data: Generation of PQPs
PeakView® Software
Notes: Synonymous of attribute analytics in MAM but at MS/MS level

## Slide 13: Column W300-25cm led to more sensitive quantification

## Slide 14: Gradient duration evaluation
DDA
SWATH

## Slide 15: Designing a sensitive and controlled acquisition method for CAR-T proteomics
Chromatography
Column:
Particle size
Length
Gradient duration
Mass Spectrometry
m/z
m/z
TOF-MS
MS/MS
s
DDA
SWATH®
m/z
m/z
Acc. time & # Precursors
Col. energ. spread
m/z
SWATH window scheme
IQ Metrics
PC
K562
Peptide Mix (e.g. PepCal)
FWHM
Ret. Times
Mass accuracy
Complex Digest (e.g. K562)
Protein ID
Quant. performances
Col #5
90 min gradient

## Slide 16: Revising the MS acquisition parameters
DDA
SWATH

## Slide 17: Designing a sensitive and controlled acquisition method for CAR-T proteomics
Chromatography
Column:
Particle size
Length
Gradient duration
Mass Spectrometry
m/z
m/z
TOF-MS
MS/MS
s
DDA
SWATH®
m/z
m/z
Acc. time & # Precursors
Col. energ. spread
m/z
SWATH window scheme
IQ/OQ Metrics
PC
K562
Peptide Mix (e.g. PepCal)
FWHM
Ret. Times
Mass accuracy
Complex Digest (e.g. K562)
Protein ID
Quant. performances
Col #5
90 min gradient

## Slide 18: Technical Variability and Devising Method Control
Peptide Mixture
Commercial complex digest
(e.g. K562 digest)
Jurkat
Notes: Quant and identficiations require a complex digest rather than peptide
Full SS reaquires a cell. While this comes with a caveat, in that will have variability when you express cells over time. Need to factor that in that biological variability will need to be addressed in a system suitability sample most likely. This is a huge challenge…

## Slide 19: Instrument and measurement control design scheme
tr
Area
m/z Calibration
K562 (D)
  # peptides ID
  # proteins ID
K562 (S)
  Select protein quant.
  PepCal spike in quant.
Use established extraction and digestion method
# of protein ID/quant.
Next Steps
  Refine digest
  Perform intermediate precision
  Set control strategy
…….
K562 (D)
Jurkat SS
Sample
PepCal IQ
……
Sample
K562 (S)
Jurkat SS
Sample
PepCal IQ
Sample
PepCal IQ
K562 (S)
K562 (S)
OQ

## Slide 20: Some specific values for the simple IQ: PepCal Mix
Example for m/z 677

## Slide 21: Some specific values for SWATH® on K562 (OQ)

## Slide 22: Preliminary application of our method on Jurkat cells
500 ng of Jurkat digest measured
~2,500 proteins quantified
Jurkat data provide us with a baseline of proteins to compare with CAR expressing Jurkat cells

## Slide 23: Steps to improve the proteomic workflow
Lombard-Banek, C. & Schiel J.E., Molecules, 2020
Enhanced protein extraction
Scalable to low amounts of samples
 Development of a model

## Slide 24: CAR-Jurkat model to advance analytics
Transduce
Express
Sort & Amplify
Before transduction
2nd sorting
Transduced to express anti-HER2 CAR (Gen 2)
Future application of this model:
  Pre/post transduction
  MQAs assessment
  In process samples for process development/monitoring
  PQAs identification and product control

## Slide 25: Evaluating different sample preparation
IS
SP3
STRAP
iST
Prot. Extr.
DIA
DDA
….
….
HPRP
DB Search
FASTA
PQPs
Qual.
Quant.
GO
Log(p-value)
Log2(FC)
Compare
Extract.
Global changes
Specific enrichment
MS1 | MS2 | RT
555.8 | 200.1 | 21
555.8 | 355.4 | 21
555.8 | 700.6 | 21
798.5 | 476.3 | 50
798.5 | 800.5 | 50
RT
Intensity
Platform agnostic WF

## Slide 26: Preliminary evaluation of sample preparation methods
CAR quant.
# Protein Quant.
Protein Abundance

## Slide 27: Conclusions
We have developed a sensitive quantitative acquisition method
We have established a measurement control strategy to collect large scale proteomic data for biotherapeutics
We are evaluating the protein extraction/digestion methods:
  # of peptides and protein identified/quantified
  Identification and coverage of the CAR
  Preparation induced modifications (e.g. M oxidation)
  Specific proteins: Jurkat functional markers (e.g. CD3, CD4, CXCR4, CD69), inflammatory proteins
Test approaches on small numbers of cells (~10,000)
Disclaimer: Instruments identification is not intended to imply recommendation or endorsement by the National Institute of Standards and Technology

## Slide 28: Acknowledgements
Schiel’s laboratory
  John Schiel
  Trina Mouchahoir
  Kat Yandrofski
  Erdem Coskun
  John Giddens
  Josh Powers
John Elliott’s laboratory
  Edward Kwee
  Sumona Sarkar
SCIEX
  Kerstin Pohl
  Melanie Juba
  David Colquhoun
  Elliott Jones